Interfacing Sensors

---
DHT11 Sensor
- Measures Temperature & Humidity
- Protocol- 1-Wire

---
Connections to Pi
Raspberry-Pi
Power
Data
Ground
5V
GPIO24
Ground
DHT11
Sensor

---
Software Dependencies
- CircuitPython
  - pip3 install adafruit-blinka
- DHT Library
  - pip3 install adafruit-circuitpython-dht
  - sudo apt-get install libgpiod2

---
Code
import time
import board
import adafruit_dht
# DHT11 device variable & data pin GPIO24:
dhtDevice = adafruit_dht.DHT11(board.D24)

---
# Run this code in forever loop
temperature_c = dhtDevice.temperature
humidity = dhtDevice.humidity
print(
        "Temp: {:.1f} C Humidity: {}% ".format(
        temperature_c, humidity
        )
)

---
Infrared(IR) Sensor
- Detects the presence of IR nearby
- Works as proximity sensor

---
Connections to Pi
Raspberry-Pi
Power
OUT
Ground
3.3V
GPIO4
Ground
IR
Sensor
Note:
OUT pin is High/1 if sensor detects IR else it is Low/0.

---
Import RPi.GPIO as GPIO
Import time
# Equivalent to GPIO4
PIN=7
# Set mode to use board pin number
GPIO.setmode(GPIO.BOARD)

---
# Input PIN for IR
GPIO.setup( PIN, GPIO.IN)
# Read input
Value = GPIO.input(PIN)

---
Ultra Sonic Sensor
- To read distance
- Configure the range of distance

---
Connections to Pi
Raspberry-Pi
5 V
GPIO14
GPIO15
Ground
Power
Trigger
Echo
Ground
Ultra Sonic
Sensor
R1
R2

---
import RPi.GPIO as GPIO
import time
#Use Board mode for GPIO
GPIO.setmode(GPIO.BOARD)
TRIG=8
ECHO=10

---
# Setting sensor
GPIO.output(TRIG, 0)
time.sleep(2)

---
print(“Pulse sent”)
GPIO.output(TRIG, True)
time.sleep(0.00001)
GPIO.output(TRIG, False)
 while not GPIO.input(ECHO):
     start = time.time()
  while GPIO.input(ECHO):
      end = time.time()

---
       duration = end - start
       distance = duration * 17150
       distance = round(distance, 2)